## Slide 1
Ultrasonic 4G NB-IoT/CAT-M1
Tekelek, Shannon Industrial Estate, Shannon, Co. Clare, Ireland
Tel : +353 (0)61 471511 E-mail: sales@tekelek.com | Web: www.tekelek.com
WEEE Reg. 00232 Patents granted
Our Ultrasonic 4G NB-IoT/CAT-M1 is a flexible and configurable battery operated liquid level sensor with an integrated Cellular modem supporting GSM (2G), LTE-CAT M1 & NB-IoT networks and GPS.
Accurate, reliable tank level monitoring
Programmable data reporting interval
Remote configurability
Easy to install
Minimum 1 year warranty
CE Conformance, ROHS and PTCRB Compliant
International Approvals
Programmable alarms
  Full alert
  Empty alert
  Spill alert (bunded tanks)
  Fill alert
  Low and High levels
  24/7 Monitoring
Benefits
Applications
Liquid level monitoring
  Fuel – Oil, Kerosene, Diesel
  Lubricants
  Additives
  DEF / AdBlue
  Coolants
  Water
  Waste Oil
  Wastewater
  Chemicals - *This product may not be suitable for monitoring of certain corrosive and hazardous chemicals. List of product compatible chemicals to be verified with a Tekelek representative.
Fixed or portable tanks
Ensure continued supply
Optimise delivery or collections
Spot and continuous inventory measurement
DS-5049-08

## Slide 2
Characteristic | Transmitter | 
Dimensions | 101mm (W) x 93mm (L) x 150mm (H) ±1mm / 4”(W) x 3.66”(L) x 5.9”(H) ±0.04” | 
Weight | 530g/1.17lbs including 4 x C size batteries - 290g/0.6lbs without batteries | 
Housing Material | UV Stabilized Polypropylene (compatible with Oil) | 
Operating Temperature | -20°C to 50°C / -4°F to 122°C (Note 1) | 
Storage Temperature | -30°C to 60°C / -22°F to 140°F (Note 1) | 
Altitude Range | <2Km/1.25miles above sea level | 
Environmental Protection | IP67 – Outdoors | 
Radio Frequency (Modem dependent) | BG96 | LTE FDD (Cat M1 & Cat NB1): B1/B2/B3/B4/B5/B8/B12/B13/B18/B19/B20/B26/B28 LTE TDD (Cat M1): B39 EGPRS: 850/900/1800/1900MHz
 | BG95 | LTE FDD (Cat M1): B1/B2/B3/B4/B5/B8/B12/B13/B18/B19/B20/B25/B26/B27/B28/B66/B85 LTE FDD (Cat NB2): B1/B2/B3/B4/B5/B8/B12/B13/B18/B19/B20/B25/B28/B66/B71/B85 EGPRS: 850/900/1800/1900MHz
GNSS (GPS) (Modem dependent) | BG96 | GPS, GLONASS, BeiDou/Compass, Galileo, QZSS
 | BG95 | GPS, GLONASS, BeiDou, Galileo, QZSS
Gauge Type | Ultrasonic | 
Ultrasonic Range | >12cm to <4m / >4.7” to 157” at 20°C(-4°F) (Note 2) | 
Ultrasonic Signal Diversion | See polar plot (Note3) | 
Ultrasonic Resolution | ±1cm / ±0.04” | 
Accuracy | Typically ±2cm from 12cm to 3m / ±0.78” from 4.7” to 118” | 
Software Features | Includes Tekelek’s advanced sonics with quality parameters | 
Material compatibility | (Note 4) | 
Power requirements | 4 of Type C LR14 Alkaline 1.5V (fitted) | 
Battery life | 5 Years (Note 5) | 
Tank mounting options | Fit directly into 1 ¼”, 1 ½” or 2” BSP existing tank connection | 
Accessories | 
SIM Card | Options available
Specification
Note 1: Storage and operation above 20°C / 68 °F may reduce battery life. Minimum distance measured is de-rated to 20cm with temperatures <0°C / 32°F
Note 2: Based on a measurement to a flat liquid target of size 30cm2 / 4.7”2
Note 3: The maximum spatial diversion of the ultrasonic signal is shown on a polar plot included with this datasheet.
Note 4: Suitable for use in tanks for the storage of water diesel fuel, kerosene, gas oil types A2,C1,C2 and D as defined by BS2869.
Note 5: Based on one data drop per day in standard configuration at a location with adequate CAT-M1/NB-IoT coverage.
Tekelek, Shannon Industrial Estate, Shannon, Co. Clare, Ireland
Tel : +353 (0)61 471511 E-mail: sales@tekelek.com | Web: www.tekelek.com
WEEE Reg. 00232 Patents granted
Conformity | 
EMC directive 2014/30/EU | The Electromagnetic Compatibility (EMC) Directive ensures that electrical and electronic equipment does not generate, or is not affected by, electromagnetic disturbance.
LVD directive 2014/35/EU | The Low Voltage Directive (LVD) ensures that electrical equipment within certain voltage limits provides a high level of protection for European citizens, and benefits fully from the Single Market.
RED directive 2014/53/EU | The Radio Equipment Directive ensures a Single Market for radio equipment by setting essential requirements for safety and health, electromagnetic compatibility, and the efficient use of the radio spectrum.
RoHs directive 2011/65/EU | This Directive lays down rules on the restriction of the use of hazardous substances in electrical and electronic equipment (EEE) with a view to contributing to the protection of human health and the environment, including the environmentally sound recovery and disposal of waste EEE.
CE compliance | Yes

## Slide 3
Specification
Tekelek, Shannon Industrial Estate, Shannon, Co. Clare, Ireland
Tel : +353 (0)61 471511 E-mail: sales@tekelek.com | Web: www.tekelek.com
WEEE Reg. 00232 Patents granted